Annex no. 1 to ref. no. PPR-4175-18/ČJ-2015-990656

Technical conditions

Technical specification and required parameters of the good:

Subject matter of public procurement

The purchase of four pieces of optoelectronic stabilized platform systems (hereinafter OSP) including training of flight and maintenance personnel.

The OSP system consists of:

- stabilized swivel heads with sensors and laser devices, operator console with display, onboard video recorder and controls

- equipment for image transmission to ground station

- moving maps of the operator.

The stabilized swivel head contains four sensors: - infrared camera with HD resolution, - day camcorder with full HD resolution, - day camcorder with powerful telephoto lens with Full HD resolution, - camcorder for low-level lighting with image chip EMCCD. Furthermore, three laser devices are placed in the head: - rangefinder, - pointer, - illuminator. The system allows for determining coordinates and distance of the target, marking targets in the image field, automatic tracking of fixed and moving targets, simultaneous display of a scene from two different sensors, and indication of moving targets. Onboard video recorder allows to record video on storage media (SSD or CF) in Full HD quality.

Image transmission to ground stations enables to broadcast video from cameras mounted in the head in DVB-T standard and Full HD quality. On-board transmitter enables to broadcast metadata (target and helicopter coordinates and other information – e.g. the distance and speed of the target) together with the video.

Moving map of the operator allows the use of raster and vector maps and different databases (e.g. database of settlements and streets of the Czech Republic). The map system is linked to the OSP system, so it is possible to control the rotating platform with cameras by marking the target directly on the map. The system also enables display of the camera's image field in the map.

Technical specification

Minimum requirements for the optoelectronic stabilized platform system (hereinafter OSP):

| Stabilised Turret with Sensors |
| --- |
| angular stability | ≤ 10 μrad |
| number of electrooptical and infrared sensors installed concurrently inside the turret | min. 4 |
| laser devices installed concurrenty inside the turret | rangefinder, illuminator and pointer |
| weight of fully equipped turret | max. 30 kg |
| operating airspeed | min. 180 knots |
| operating temperature | -30°C až +45°C |

| Airframe Mount of the Stabilised Turret |
| --- |
| possibility of easy and quick installation and removal during the EC135 helicopter operation | yes |
| Sensor No.1 – Infrared Camera |
| wavelenght | in the band of 5 μm |
| detector size | min. 1280 x 720 |
| optical field of view | min. 30° to 2°, continuous zoom |
| DRI (man size target, ΔT=2°C, σ=0.2 km-1) | min. 6 km, 3 km, 1.5 km |

| Sensor No.2 – Electrooptical Camera |
| --- |
| wavelenght | in the band of visible light |
| detector size | 1920 x 1080 |
| optical field of view | min. 30° to 1.5°, continuous zoom |
| DRI (man size target, visibility >20 km) | min. 8 km, 4 km, 2 km |

| Sensor No.3 – Electrooptical Camera 2 (SPOTTER) |
| --- |
| wavelenght | in the band of visible light |
| detector size | 1920 x 1080 |
| optical field of view | max. 0.5° |
| DRI (man size target, visibility >20 km) | min. 8 km, 4 km, 2 km |

| Sensor No.4 – Low Light Camera |
| --- |
| wavelenght | in the band of visible light |
| detector size | min. 640 x 480 |
| type of detector | EMCCD |
| optical field of view | max. 1.5° |
| DRI (man size target, visibility >20 km, full Moon) | min. 5 km, 1.5 km, 1 km |

| Video Format (refers to all sensors) |
| --- |
| digital video resolution | 1080p, 720p |
| digital video format | MISP & STANAG 4609 SMPTE-292M / 1080p |
| analog video | PAL |

| Laser Device No.1 - Rangefinder |
| --- |
| class | Class 1 (eyesafe) |
| range | min. 20 km |

| Laser Device No.2 - Illuminator |
| --- |
| wavelenght | 850 nm |
| power | min. 700 mW |

| Laser Device No.3 - Pointer |
| --- |
| wavelenght | 850 nm |
| power | min. 150 mW |

Other Required Functions of the System

target coordinates and range info

possibility of saving targets to memory

GEO pointing and target tracking

dual veiw capability

moving target indicator

metadata embedded in videostream

| Displays of the Operator |
| --- |
| digital video format | MISP & STANAG 4609 SMPTE-292M / 720p a 1080p |
| resolution | 1920 x 1080 |
| contrast ratio | min. 500:1 |
| LCD response | max. 25 ms |

| Operator Console |
| --- |
| suitable for fitting of two displays (map + video) | yes |
| all controls of the system can be comfortably reached by the operator | yes |
| enables position adjustment of displays and controls | yes |

| Downlink System |
| --- |
| frequency range | 2.0 – 2.5 GHz |
| output transmitting power | min. 8 W |
| modulation | COFDM (DVB-T) |
| bandwidth | 6 MHz, 7 MHz, 8 MHz |
| video input | SMPTE 292M, PAL |
| MPEG coding | H.264/MPEG-4 |
| MPEG format | 1080p/30, 720p/60, 576i (PAL) |
| metadata embedded in videostream | yes |
| encryption | AES 128/256 |
| weight of the transmitter | max. 5 kg |
| portable receiver (handheld preferred) | yes |

| Videorecorder |
| --- |
| location | in comfortable reach of the operator |
| weight | max. 2 kg |
| media | CF, USB or SD |
| video input | HD-SDI a SD-SDI (SMPTE) |
| video output | HD-SDI a SD-SDI (SMPTE) |
| resolution | 1080p25/30, 1080i50/60, 720p25/30 |
| digital audio recording | yes |
| onboard playback | yes |
| easy playback of the videofile on PC (without conversion) | yes |
| Moving Map System |
| control panel lighting | NVG compatible |
| map formats | raster, photo, vector |
| two independent outputs | yes |
| user databases | yes |
| map with street database of the Czech Republic | yes |
| flight planning and recording | yes |
| display of map vector data in the camera picture (ARS) | yes |
| interface with FLIR system | yes |
| interface with EC-135 navigation systems | yes |

Other requirements

The system and its components must be approved according to applicable aviation regulations and related regulations.

The subject of the public procurement is the delivery of all parts of the system defined by the minimum requirements, including all peripheral devices, antennas, special installation fittings and other special hardware, and the training of flight personnel, including technical service and maintenance personnel. The subject matter is not regular installation material.

Annex no. 2 to ref. no. PPR-4175-18/ČJ-2015-990656

    - Bid cover sheet for the public procurement

Purchase of 4 pc of optoelectronic stabilized platform systems for EC-135 T2+ helicopters

Bidder:

Name, legal form:

Address:

Represented by:

Identification number:

Tax identification number:

Bank details:

Account number:

Contact person:

Telephone:

Fax:

E-mail:

Registered in the …….…….. register, maintained by ……..….., at the court in ………………., section …….….., insert ………..

Period of performance: …………………………...........................................................................

The bidder declares that the goods meet the requirements of the Contracting Authority in terms of performance and functionality as required in the tender documentation.

The bidder declares that prior to submitting the bid he has clarified all the necessary information that uniquely define the performance of this public contract.

The bidder declares that the submitted bid contains all the documents required by the Contracting Authority in the tender documentation ref. no. PPR-4175-18/ČJ-2015-990656 and that these are clear and understandable.

The bidder declares that he accepts the terms set out by the Contracting Authority in the tender documentation ref. no. PPR-4175-18/ČJ-2015-990656, and these clear and understandable.

In ………………  date………

_____________________

Signature of authorized person/s

(title, name, surname)

Annex no. 3 to ref. no. PPR-4175-18/ČJ-2015-990656

Template binding text of the purchase contract

Purchase contract

Ref. no. PPR-4175-??/ČJ-2015-990656

- Purchaser:				CZECH REPUBLIC

- Interior Ministry

Address:					Prague 7, Nad Stolou 936/3, 170 34

Legal form:				325-goverment department

Identification number:			00007064

Tax identification number:			CZ00007064

Represented by:				Ing. Miroslav Hajný

Director Department of Logistic Administration of the Police Presidium Czech Republic

Bank details:				Czech National Bank

Account number:				5504881/0710

Tel.:					974 884 513

Contact person:				Ing. Václav Sládeček

Tel: 					974 838 249

(hereinafter „purchaser“) as one party

and

Seller:					[!TO BE COMPLETED BY THE SELLER!]

Address:					[!TO BE COMPLETED BY THE SELLER!]

Identification number:			[!TO BE COMPLETED BY THE SELLER!]

Tax identification number:			[!TO BE COMPLETED BY THE SELLER!]

Registered in the commercial register	[!TO BE COMPLETED BY THE SELLER!]

Represented by:	 			[!TO BE COMPLETED BY THE SELLER!]

Bank details:				[!TO BE COMPLETED BY THE SELLER!]

Account number:				[!TO BE COMPLETED BY THE SELLER!]

Contact person:				[!TO BE COMPLETED BY THE SELLER!]

Tel.:					[!TO BE COMPLETED BY THE SELLER!]

Fax:					[!TO BE COMPLETED BY THE SELLER!]

E-mail:					[!TO BE COMPLETED BY THE SELLER!]

(hereinafter „seller“) as the second party

are concluding

according to § 2079 et. seq. of Act no. 89/2012 Coll., Civil Code (hereinafter „Civil Code“) this

purchase contract (hereinafter „contract“)

I.

- Subject matter of the contract

/1/	With this contract, the seller undertakes to supply the goods referred to in Article II. Sec. / 1 / to the purchaser under the conditions stipulated in this contract and transfer the right of ownership of the goods to the purchaser.

/2/	The purchaser shall accept the goods and pay the agreed purchase price in the manner and within the deadline set forth herein.

/3/	The contract was concluded on the basis of the contracting authority's decision on the selection of the best bid of the public tender according to § 21 paragraph 1 letter a) of Act
no. 137/2006 Coll. On Public Procurement (hereinafter “the Act”) published in the Bulletin of Public Tenders dated …. registered under Nr. ….

- II.

- Goods

- Goods mean the delivery of 4 pc of optoelectronic stabilized platform systems for EC-135 T2+ helicopters including training of flight and maintenance personnel.

- The technical specification of the goods is listed in annex no. 1 (Specification of the goods), which is an integral part of this contract.

- The seller undertakes to deliver new goods, the purchaser will be the first user, and in the current production version of the products.

- The purchaser shall acquire ownership rights to the goods upon acceptance of the goods from the seller.

- III.

- Date of fulfilment

- The seller shall deliver the goods to the purchaser by 15th December 2015.

- The seller undertakes to inform the purchaser about the date of delivery of the goods at least five working days in advance through the person responsible for the acceptance of the goods. Risk of damage to the goods passes to the purchaser upon acceptance of the goods from the seller.

- In case of delay in delivering the goods, the seller shall pay a penalty of 0.05% of the price of the goods including VAT for each day of delay, which were not delivered in time in accordance with the provisions of Art. III. Sec. /1/ of this contract, whereas the price of the goods is specified in Art. IV. Sec. /1/ and /2/ of this contract. The seller is obliged to pay the purchaser the agreed contractual penalty within 30 days from the date when the written bill was delivered from the purchaser to the seller. In case of doubt about the date of delivery, the date of delivery shall be deemed the third day after the purchaser sent the bill.

- IV.

- Price of goods

- The purchase price of the goods incl. shipping, packaging and training of flight staff and ground technicians is the maximum permissible price, a change is permissible only if the statutory VAT changes.

- The agreed purchase price for the goods excluding VAT is CZK [!TO BE COMPLETED BY THE SELLER!] (in words: [!TO BE COMPLETED BY THE SELLER!]Czech Crowns), VAT 21 % is CZK [!TO BE COMPLETED BY THE SELLER!] and the total price for the goods including VAT is CZK [!TO BE COMPLETED BY THE SELLER!] (in words: [!TO BE COMPLETED BY THE SELLER!]Czech Crowns).

- V.

- Payment conditions

- The seller shall send an invoice to the purchaser within 5 days from delivery of the goods.

- Tax documents must meet the requirements specified in § 29 of Act no. 235/2004 Coll., On Value Added Tax, as amended. Invoices must meet all the requirements set by the Czech legislation, particularly § 435 of the Civil Code. In addition to these requirements, the invoice shall contain an indication of the bidder, purchaser (Czech Republic – Interior Ministry, Nad Stolou 936/3, 170 34 Prague 7) and the invoice recipient (Czech Police Aviation Department, Post office 614, Box 35, 161 01 Prague 6). Each invoice (tax document) shall be issued in two copies (1 original + 1 copy).

- The purchaser is obliged to pay the invoice within 30 days from receipt. In case of doubt, it is considered that the date of receipt is the third day after the invoice was sent.

- In case of delay, the contracting parties have agreed:

- On a contractual penalty in the amount of 0.05% of the price of the goods including VAT for each delayed day, which the seller is obliged to pay to the purchaser within 30 days after receipt of the written bill of the contractual penalty for failure to perform obligations according to Art. V. Sec. /3/ of this contract,

- On a statutory default interest on the invoice price of the goods including VAT for each delayed day, which the purchaser is obliged to pay to the seller within 30 days after receipt of the written bill of the statutory default interest for failure to perform obligations according to Art. V. Sec. /3/ of this contract.

- The purchaser does not provide advance payments.

- VI.

- Delivery and acceptance of the goods

- Place of delivery of the goods is the Czech Police Aviation Department, K Letisti – Gate 1, hangar D, 160 00 Prague 6 Ruzyne.

- An inspection of all functionalities of the goods shall be carried out upon acceptance of the goods. The training of flight staff and ground technicians shall be carried out consequently. The seller shall provide operator and maintenance training for authorized staff of the purchaser. The training shall be conducted by the seller or authorized training centre.

- Generally applicable legislation applies to the acceptance procedure. Acceptance shall be performed by a representative of the purchaser.

- The goods will be delivered to the purchaser upon acceptance of the goods and confirmation of a delivery or acceptance note at the place of delivery. The employee authorized to sign the delivery note and accept the goods is Ing. Václav Kricner, tel. 974 838 214.

- The purchaser is obliged to inform the seller of defects upon acceptance, which are apparent during delivery of the goods; the purchaser is obliged to inform the seller of hidden defects without undue delay.

- VII.

- Warranty for quality of goods

- The seller shall provide warranty service for 24 months from delivery and acceptance of the goods for all infrastructure components.

- The address of the service centre and contact person including telephone contact: [!TO BE COMPLETED BY THE SELLER!]

- The warranty period begins from the date of acceptance of the goods by the purchaser. The warranty period ceases to run for the period when the purchaser cannot use the goods due to defects for which the seller is responsible.

- The period for settling claims is 30 days from the date of receipt of the complaint protocol to the seller. In case of doubt, the date of receipt means the third day after the protocol is sent by the purchaser. If the period for the settling claims will require more than 30 days, the period will be determined by an agreement of the contracting parties.

- The warranty claims for defective goods shall be resolved within the warranty period through repair or exchange for a faultless item, claims shall be lodged in the Czech Republic.

- In case of a delay in the date according to Art. VII. Sec. /4/, the contracting parties agree on a contractual penalty in the amount of CZK 1000 (in words: one thousand Czech Crowns) for each delayed day, which the seller is obliged to pay to the purchaser within 30 days after receipt of the billing of the contractual penalty.

- VIII.

- Other provisions

- The seller agrees to maintain confidentiality in relation to third parties on information that he receives from the purchaser or about the purchaser or his employees and colleagues during performance of this contract and shall not disclose this information to third parties nor use it contrary to the purpose of this contract without written consent of the purchaser, unless

  - the information is publicly available, or

  - it is a case, in which disclosure of information is required by the law or binding decision of a competent authority.

- The seller is obliged to bind all persons who participate in the delivery of the goods to the contracting authority with the obligations of confidentiality according to Art. VIII. Sec./1/ of this contract.

- The seller is responsible for breach of confidentiality by persons participating in the delivery of the goods, as if he breached this obligation himself.

- Duty of confidentiality continues even after termination of effectiveness of this contract.

- Each contracting party shall promptly notify the other contracting party in writing of any changes in the data listed in the heading of this contract.

- The seller declares that the goods referred to in Art. II. Sec. /1/ of this contract has no legal defects within the meaning of provisions §1920 of the Civil Code.

- In case of violation of the obligations specified in more detail in Art. VIII. Sec. /1/ to /4/ and /6/ of this contract, the seller is obliged to pay a contractual fine in the amount of CZK 100,000.00 (in words: one hundred thousand Czech Crowns) payable within 30 days from the date of billing by the purchaser.

- The seller shall provide the purchaser with a list of subcontractors stating the subcontractors to which he has paid more than 10% of the total contract price. The seller shall submit a list of subcontractors within 60 days of completion of the contract. If it is a joint stock company, a list of owners of shares whose nominal value exceeds 10% of capital shall be attached to the list, completed within 90 days prior to the date of submission of the list of subcontractors. For failure to comply with this obligation, the seller is obliged to pay a contractual penalty in the amount of CZK 200,000.00 (in words: two hundred thousand Czech Crowns) payable within 30 days from the date of billing by the purchaser.

IX.

Obligations of the seller

Because the project “Aviation technology for rescue work in the IRS system” CZ.1.06/3.4.00/27.09721 is co-financed from EU structural funds within the framework of the Integrated Operational Programme, the seller is obliged to:

/1/	Duly keep all documentation related to the implementation of the public procurement, including accounting documents at least until 31st December 2025, and if the Czech legislation specifies a period longer than the European legislation, the longer period must be used.

/2/	Provide the required information and documentation to employees and agents of designated authorities (Department of Structural Funds of the Interior Ministry Czech Republic, the Ministry for Regional Development Czech Republic, Ministry of Finance Czech Republic, the European Commission, the European Court of Justice, the Supreme Audit Office, the competent financial authority and other authorized bodies of state administration) for a period of ten years for the purpose of verifying compliance with obligations arising from the conditions of the Operational Programme and enable to those referred to above the conditions to implement checks relating to the implementation of the public procurement and provide them cooperation when conducting inspections

/3/	The seller is obliged to ensure that the above mentioned obligation in relation to the subject matter of the contract is performed by all subcontractors participating in this contract.

/4/	All material related to the project (contracts concluded within the framework of the project, written correspondence related to the project, written reports, tangible and written output, presentations etc.) must be labelled in accordance with the handbook for applicants and beneficiaries resp. with the document “Guidelines for the implementation of information and publicity measures”, which is a part of the annexes of Call no. 27 of the Integrated Operational Programme (specifications for size and colour), and the IOP Logo Manual. All logos in various graphic formats according to needs and the valid IOP Logo Manual can be found at www.strukturalni-fondy.cz/iop. This obligation of the beneficiary to carry out informational and promotional measures is based on the regulation of the European Commission (ES) no. 1828/2006 and no. 846/2009. Below is the recommended format of this labelling:

/5/	Each accounting document shall be labelled with the project number and the information that it is a project co-financed by IOP and ERDF, in the following manner:

“Project „Aviation technology for rescue work in IRS“, registration number CZ.1.06/3.4.00/27.09721 is co-financed by the European Union, European Regional Development Fund within the framework of the Integrated Operational Programme.”

The seller declares that he is familiar with these guidelines on the effective date of this contract. In the event that during the performance of this contract there is a change to these rules, the purchaser shall immediately inform the seller about this.

X.

- Common and final provisions

- The mutual relationships between the contracting parties, which are not specifically agreed in this contract, shall be governed by the relevant provisions of the Civil Code.

- The provisions regarding contractual penalties do not affect the right of the purchaser to claim damages from the seller, which shall be claimed by the responsible officer of the Department of Logistic Administration of the Police Presidium of the Czech Republic.

- All contractual penalties under this contract that the seller is obligated to pay to the purchaser shall be claimed by the responsible officer of the Department of Logistic Administration of the Police Presidium Czech Republic.

- The purchaser is entitled to withdraw from the contract in the event of a material breach of the contract by the seller. Material breach is considered in particular:

-	delay in the delivery of the goods by the seller by more than 30 days,

-	false or misleading declarations made by the seller according to Art. VIII. Sec. 1 to 4 and 6.

- Furthermore, the purchaser is entitled to withdraw from the contract in the event that:

-	there is an insolvency proceeding against the seller, in which the decision on bankruptcy was issued, if legally permissible,

-	a bankruptcy petition on the seller was dismissed because the seller’s assets are insufficient to cover the costs of insolvency proceedings,

-	the seller enters into liquidation.

- The seller is entitled to withdraw from the contract if the purchaser is in arrears with the payment of an invoice for more than 30 days from the due date of the invoice.

- Withdrawal shall become effective on the date of receipt of the written notice to the other contracting party.

- The seller is obliged to keep documents related to the sale of goods under this contract for at least ten (10) years from the end of the accounting period in which the last payment for the goods was made, respectively the last taxable performance under this contract, namely for control purposes of authorized enforcement authorities.

- The seller is obliged to cooperate in the performance of financial control according to § 2 letter e) of Act no. 320/2001 Coll., on Financial Control in Public Administration, as amended (Act on Financial Control).

- The seller agrees that entities authorized under the Act on Financial Control implement financial control of the contractual relationship arising from the contract.

- The seller is obliged to notify the purchaser in writing about existing or impending conflicts of interest immediately after the conflict of interest arises or becomes apparent in the case that the sellers exerting professional care could not detect a conflict of interest prior to the conclusion of this contract. Conflict of interest means the activity of the seller, due to which there would be a fulfilment of law no. 159/2006 Coll., On Conflict of Interest, namely § 2 par. 3 letter b) and § 3 par. 2 letter a).

- The seller is obliged to inform the purchaser about fulfilling the condition stated in § 81 of Act no. 435/2004 Coll., On Employment, if it is met.

- The seller without any objection agrees to publish his identification and other information included in the contract, including the price of goods.

- The contracting parties hereto agree that any disputes arising in connection with the contract shall be resolved amicably – by agreement. If no agreement is reached, disputes will be resolved before competent courts.

- The seller shall not assign or transfer any rights or obligations arising under the contract to any third party without prior express written consent by the purchaser.

- Part of this contract is annex no. 1 (Specification of the goods).

- This contract may be changed and supplemented only after agreement of both contracting parties in written form as numerically labelled amendments to this contract.

- The contract is executed in five counterparts, each with the validity of the original, of which the purchaser shall receive four and the seller one.

- The contract takes effect and comes into force on the date of conclusion by both contracting parties.

| In .............................date.........….....2015 …………………………………………….. |  | In Prague date……….....……….2015 ………………………………………… Ing. Miroslav Hajný Director of Department of Logistic Administration of the Police Presidium Czech Republic |
| --- | --- | --- |
| seller (stamp, signature) |  | purchaser (stamp, signature) |

Annex no. 1 of the Purchase contract

SPECIFICATION OF THE GOODS

To be completed by the bidder

Annex no. 4 to ref. no.: PPR-4175-18/ČJ-2015-990656

T E M P L A T E

AFFIDAVIT

for demonstrating basic qualification requirements in accordance with provisions § 53 of Act no.137/2006 Coll., on Public Procurement, as amended (the "Act)

We hereby declare, that:

- we have not fulfilled facts of unfair competition in the form of bribery pursuant to § 2983 of Act no. 89/2012 Coll., The Civil Code (§ 53 par. 1 letter c) of Act no. 137/2006 Coll., On Public Procurement, as amended, (hereinafter “the Act”) in the last three years,

- there is no insolvency proceeding against our assets, or in the last three years there was no insolvency proceeding, in which a decision on bankruptcy was issued or a bankruptcy petition was dismissed because the assets were completely insufficient or put under receivership according to special laws (§ 53 par. 1 letter d) of the Act),,

- we have not entered into liquidation (§ 53 par. 1 letter e) of the Act),

- we have no records of tax arrears in respect of excise duty, both in the Czech Republic and in the country of residence, place of business or residence (§ 53 par. 1 letter f) of the Act),

- we have no outstanding premiums and penalties for public health insurance, both in the Czech Republic and in the country of residence, place of business or residence (§ 53 par. 1 letter g) of the Act),

- we are not in the register of persons prohibited from performing public contracts (§ 53 par. 1 letter j) of the Act) and

- we have not been in the last three years, fined for allowing illegal work under a special law (§ 53 par. 1 letter k) of the Act).

In…………………date……………………..

…………………………………………..

Name (in block letters) and signature

of the authorized representative of the bidder

Annex no. 5 to ref. no. PPR-4175-18/ČJ-2015-990656

AFFIDAVIT

for demonstrating economic and financial capacity to fulfil the public contract in accordance with the provisions § 50 par. 1 letter c) of Act no. 137/2006 Coll., on Public Procurement, as amended, (the "Act")

COMPANY:

………………………………………………………………………………………………

In accordance with the requirements of Act no. 137/2006 Coll., for demonstrating the economic and financial capacity to fulfil the public contract pursuant to § 50 par. 1 letter c) of the Act, as we, as the bidder for this public contract, attest following affidavit:

I hereby declare, in accordance with § 50 par. 1 letter c) of the Act, that as the bidder for this public contract, we are economically and financially qualified to fulfil the public contract.

In…………..date ……………..

…………………………………………..

Name and signature

of the authorized representative of the bidder

Annex no. 6 to ref. no. PPR-4175-18/ČJ-2015-990656

Documents in accordance with § 68 par. 3 of Act 137/2006 Coll., On Public Procurement, as amended (the "Act")

In accordance with the requirements of § 68 par. 3 of the Act we provide the following facts and documents, by which we attest additional information about our company. I declare that all the following information is true.

- List of statutory bodies or members of statutory bodies, which have been in a labour-, functional- or similar relationship with the contracting authority in the last 3 years before the deadline for submission of bids:

- ………………………(or state that no such persons are in the above mentioned bodies)

- List of shareholders with an aggregate nominal value exceeding 10% of the basic capital in the period for submitting bids:

- …………………………………… (shall be indicated in the case that the bidder is a joint-stock company – or state that it is not a joint-stock company)

- I declare that as a bidder for this public contract, I have not concluded and will not conclude a prohibited agreement under a special law in relation this public procurement.

In…………………date……………………..

……………………………………

Name and signature

of the authorized representative of the bidder

Annex no. 7 to ref. no. PPR-4175-18/ČJ-2015-990656

Affidavit

I, the undersigned ................................., as the person authorized to act on behalf of the bidder honestly declare that I agree with all the terms of the tender documentation and its annexes.

In…………………date……………………..

……………………………………

Name and signature

of the authorized representative of the bidder

Annex no. 8 to ref. no. PPR-4175-18/ČJ-2015-990656

Affidavit

I, the undersigned ................................., as a person authorized to act on behalf of the bidder honestly declare that the goods specified in the bid meet the parameters stated in the tender documentation and its annexes.

In…………………date……………………..

……………………………………

Name and signature

Of the authorized representative of the bidder